## Slide 1
CprE 381: Computer Organization and Assembly Level Programming
Virtual Memory
Berk Gulmezoglu
Electrical and Computer Engineering Iowa State University

## Slide 2: Remember the System View!
Peripherals
Input
Output
Memory
Processor
Control
Datapath
A Computer
Lec14.1.2

## Slide 3: Virtual Memory
Use main memory as a “cache” for secondary (disk) storage
  Managed jointly by CPU hardware and the operating system (OS)
Programs share main memory
  Each gets a private virtual address space holding its code and data
  Frequently used code and data pulled into main memory
  Protected from other programs
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called a page
  VM translation “miss” is called a page fault

## Slide 4: Address Translation
Fixed-size pages (e.g., 4K)
Main Memory  seen as a cache for disk

## Slide 5: Page Fault Penalty
On page fault, the page must be fetched from disk
  Takes millions of clock cycles
  Handled by OS code
Try to minimize page fault rate
  Fully associative placement
  Smart replacement algorithms

## Slide 6: Page Tables
Stores placement information
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  PTE stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk

## Slide 7: Translation Using a Page Table

## Slide 8: Mapping Pages to Storage

## Slide 9: Replacement and Writes
To reduce page fault rate, prefer least- recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Block at once, not individual locations
  Write through is impractical
  Use write-back
  Dirty bit in PTE set when page is written

## Slide 10: Page Table Size
Calculate the size of a page table
  32-bit virtual address
  4KB pages
  4 byte page table entries (PTEs)

## Slide 11: Page Table Size
Calculate the size of a page table
  32-bit virtual address
  4KB pages  page offset is 12 bits
  4 byte page table entries (PTEs)
# PTEs = 2# bits in virtual address / 2# bits page offset
= 232/212 = 220
PT Size = # PTEs * PTE Size
= 220 PTEs * 22 bytes/PTE = 4 MB

## Slide 12: Page Table Size
Calculate the size of a page table
  64-bit virtual address
  16KB pages  page offset is 14 bits
  8 byte page table entries (PTEs)
# PTEs = 2# bits in virtual address / 2# bits page offset
= 264/214 = 250
PT Size = # PTEs * PTE Size
= 250 PTEs * 23 bytes/PTE = 8 PB

## Slide 13: Page Table Size
•
Calculate the size of a page table
– 64-bit virtual address
– 16KB pages  page offset is 14 bits
– 8 byte page table entries (PTEs)
PTEs = 2# bits in virtual address / 2# bits page
= 264/214 = 250
#
offset
PT Size = # PTEs * PTE Size
= 250 PTEs * 23 bytes/PTE = 8 PB
Blue Waters Supercomputer: 1.5PB Memory

## Slide 14: Acknowledgments
These slides contain material developed and copyright by:
  Joe Zambreno (Iowa State)
  Akhilesh Tyagi (Iowa State)
  David Patterson (UC Berkeley)
  Mary Jane Irwin (Penn State)
  Christos Kozyrakis (Stanford)
  Onur Mutlu (Carnegie Mellon)
  Krste Asanović (UC Berkeley)
  Morgan Kaufmann